Midi Controller

for
Zoom MS-50G, MS-70CDR, G5, G3

Developed by
Massimo Procopio

www.massimoprocopio.com

VintgSol

M = Mode Footswitch
L = Left Footswitch (Footswitch 1)
C = Central Footswitch (Footswitch 2)
R = Right Footswitch (Footswitch 3)
K = Knob
PWR = Power 9V DC
USB = USB Out for Zoom
EXT (Optional) = Connector(s) to add max 3 Footswitches (4, 5, 6)

K
M
L
C
R
USB
EXT
PWR
Minimum Configuration

 - -------------- +
23
Blues OD

M = Mode Footswitch
L = Left Footswitch (Footswitch 1)
C = Central Footswitch (Footswitch 2)
R = Right Footswitch (Footswitch 3)
K = Knob
PWR = Power 9V DC
USB = USB Out for Zoom
4 = Footswitch 4
5 = Footswitch 5
6 = Footswitch 6

K
M
L
C
R
USB
PWR
4
5
6
Maximum Configuration
 - -------------- +
23
Blues OD

Modes

Normal Mode

 - -------------- +
23
Blues OD

▇Room
 ZNR
▇CarbonDL
>> E-EFFECTS 0 <<
▇AnalogDL
▇MetlWRLD
 Graph EQ
E-Patch Mode
E-Effects Mode

M

M

Press Mode Footswitch or Knob
Press Mode Footswitch or Knob

M
Press Mode Footswitch or Knob

Blues OD
MetalZon
Delay OD
 - EP-0
Rat Driv
▇MetalDis
Clean
VintgSol

Preselect
Select

Select Up and Down

 - -------------- +
23
Blues OD
Preselect Up and Down

C

C

Press Central Footswitch
Press Central Footswitch

 - <<<<<-->>>>> +
29
Delay C1

 - -------------- +
29
Delay C1
Patch Selected
L
R
Down
Up
L
R
Down
Up

Patch 29 Activated

Normal Mode

Up and Down Bank
M
Press Mode Footswitch

M
Long Press Mode Footswitch
E-Patch Mode
L
MetalZon
L
Blues OD
C
Delay OD
C
Blues OD
R
VintgSol
R
Blues OD
4
Rat Driv
4
Blues OD
5
MetalDis
5
Blues OD
6
Clean
6
Blues OD
L
Down
R
Up
VintgSol

M
Press Mode Footswitch

Each Effect is assigned to a Footswitch. Pressing it, the related effect is activated ▇ or disactivated ☐

M
Long Press Mode Footswitch
C
R
4
L
AnalogDL
MetlWRLD
Graph Eq
5
ZNR
6
Carbon DL
L
R

▇Room
 ZNR
▇CarbonDL
>> E-EFFECTS 0 <<
▇AnalogDL
▇MetlWRLD
 Graph EQ

▇Room
 ZNR
▇CarbonDL
     <<< >>> 0
▇AnalogDL
▇MetlWRLD
 Graph EQ

▇Room
 ZNR
▇MetlWRLD
>> E-EFFECTS 1 <<
▇AnalogDL
▇CarbonDL
 Graph EQ
Up and Down Bank

Down
Up
E-Effects Mode
Room

In the Effects Mode, each bank has a sequence of effect numbers. For 6 footswitches configuration it is enough only one bank with the sequence 1, 2, 3, 4, 5, 6. When you change patch, effects are rescanned to update the effects names and status. If you change the effect type or status directly from the Zoom controls, it will be updated on the Midi Controller automatically.

Soul
Metal2
Delay C1
 - EP-3
Rat Driv
Tone3
Dist
Flanger

Blues OD
MetalZon
Delay OD
 - EP-0
Rat Driv
▇MetalDis
Clean
VintgSol

Blues OD
MetalZon
Delay OD
<<< >>> 0
Rat Driv
▇MetalDis
Clean
VintgSol
Each Patch is assigned to a Footswitch. By pressing it again, the controller goes back to the base patch (Blues OD in this case). Symbol ▇ shows the activate patch.

...
- Cancel
- Bank 0 to 49

Allowed only in Patch Mode or Effects Mode
- Cancel
- Basic Patch
- Footswitch 1 to 6
- Cancel
- Bank 0 to 49
- Cancel
- Effect 1 to 6
- Cancel
- Effect 1 to 6
- Cancel
- Effect 1 to 6
- Cancel
- Bank 1 to 9

SELECT DEST BANK:
Cancel
CLONE BANK

CLONE BANK <
ASSIGN PATCH
ASSIGN EFFECT
SET FOOTSWITCHES
K
Long Press Knob to enter in the menù
Menù

TOGGLE MODE <
LONG PRESS DELAY
STARTING MODE
RESET MEMORY

STARTING MODE
RESET MEMORY
FIRMWARE
EXIT <
K
Rotate Knob to move between menù settings
K
Press Knob to Enter

SELECT FOOTSWITCH:
Cancel
ASSIGN PATCH

SELECT BANK:
Cancel

FOOTSWITCH 1 EFF.:
Cancel
ASSIGN EFFECT

FOOTSWITCH 2 EFF.:
Cancel

FOOTSWITCH 6 EFF.:
Cancel

SELECT BANK:
Cancel

K
Long Press Knob to enter in the menù
Menù
K
Rotate Knob to move between menù settings
K
Press Knob to Enter
- 3 to 6
- All Modes
- E-Patch – E-Effects
- Normal – E-Effects
- Normal – E-Patch
- 250 to 5000 ms
- Normal Mode
- E-Patch Mode
- E-Effect Mode
- Cancel
- Reset All Memory

FOOTSWITCHES NUM:
3
SET FOOTSWITCHES

TOGGLE MODE:
ALL MODES
TOGGLE MODE

CHANGE PRESS DELAY:
750 ms
LONG PRESS DELAY

CHOOSE MODE:
NORMAL MODE
STARTING MODE

RESET MEMORY:
CANCEL
RESET MEMORY

Firmware Version
2.2.800
FIRMWARE

23
Blues OD
EP
1
      --------------
E-Patch Mode
Selected Patch.

 - -------------- +
23
Blues OD
Normal Mode

 > ..... ..... <
23
Blues OD
Normal Mode
Actual Patch is changed by using Zoom.
By pressing Left or Right footswitches, the controller goes up or down from this position.
Selected Patch.
E-Patch Bank 1.
This is shown for few seconds when it is pressed a Footswitch.

23
Blues OD
EP
1
 > ..... ..... <
E-Patch Mode
Actual Patch is changed by using Zoom.
E-Patch Bank 1.
By pressing an assigned footswitch, the controller actives the related patch and it goes back to the E-Patch mode normal graphics.

Double direction synchronization examples
Notes for Zoom MS-50G and MS-70CDR
It is possible to use the Zoom pedal as if there was no controller, but I suggest to set an A and B patches with the same duplicated patch (different names), so the zoom pedal actives always the same patch, adding one more patch control, easily available. With the 6 footswitches configuration, in this way, in E-Patch Mode the user will have an easy control of 8 patches: Basic Patch , 6 Assigned, and one on Zoom (A-B toggle). This mode is also convenient to see the activated patch on zoom display. Press at least one time the zoom footswitch to activate this visualization. It is possible also to use the long press on Zoom for the tuner or to change tap tempo.
# License Information

Released Under GPL License.
You are allowed to copy, modify and redistribuite it in accordance with the provisions of the GPL licenses. You are required to maintain the original copyright notices, including the name of the first developer, and to distribute your modified version under the same GPL terms.

Massimo Procopio	14/06/2025